## Slide 1: MassDEP Sampling in Mystic Lakes
Photo: Spy Pond Park, Brandon Bushey

## Slide 2: Mystic Lakes Impairments
Name | ID | Location | Size (Acres) | Draft 2016 IR Category 5
Horn Pond | MA71019 | Woburn | 108 | (Non-Native Aquatic Plants**) DDT in Fish Tissue, Harmful Algal Bloom, Oxygen, Dissolved Phosphorus (Total)
Spy Pond | MA71040 | Arlington | 98 | (Eurasian Water Milfoil, Myriophyllum spicatum**) Chlordane in Fish Tissue, DDT in Fish Tissue, Harmful Algal Bloom, Oxygen, Dissolved Phosphorus (Total)
Wedge Pond | MA71045 | Winchester | 23 | Harmful Algal Bloom Oxygen, Dissolved Phosphorus (Total)
Mystic Lakes Impairments

## Slide 3: EPA Alternative TMDL work
Watersheds and Loadings for the three ponds have been calculated
This work can be used in a Lake Loading Response Model
Updated, recent water quality sampling data is needed
EPA Alternative TMDL work

## Slide 4: Mystic Lakes 2019 Sampling
3 ponds (Horn Pond, Wedge Pond and Spy Pond)
Index site sampling at deep hole
  4 visits (June to October)
  Surface and Bottom Nutrients (TN,TP)
  Depth Integrated Chlorophyll a
  Dissolved Oxygen Profile
Bathymetric Mapping Once Each Pond

## Slide 5: Ponds/Lake Analysis Team
Ponds/Lake Analysis Team includes: Al Basile (EPA), Barbara Kickham (MassDEP), Matthew Reardon (MassDEP), Toby Stover (EPA), and Mark Voorhees (EPA)
  Contact Information
Matthew Reardon (508-849-4002)
  Matthew.Reardon@mass.gov